HIGH PRESSURE WASHER

ORIGINAL INSTRUCTIONS

HNHP2200-165ACCR

English

The symbol on the product or on its packing indicates that this product may not be treated as household waste. Instead it shall be handed over

To the applicable collection point for the recycling of electrical and electronic equipment. By ensuring this product is disposed of correctly, you will help prevent potential negative consequences for the environment and human health, which could otherwise be caused by inappropriate waste handling of this product. For

more detailed information about recycling of this

product, please contact your local city office, your household waste disposal service or the shop where you purchased the product.

Deutsch

Das Symbol auf dem Produkt bzw. auf der Produktverpackung deutet an, dass das Produkt nicht mit dem Haushaltsmüll entsorgt werden darf. Stattdessen ist es zur Entsorgung an eine geeignete Sammelstelle für das Recycling von elektrischen und elektronischen Geräten zu bringen. Durch die korrekte Entsorgung helfen Sie mit, potenziellen negativen Einflüssen auf die Umwelt und die Gesundheit vorzubeugen, die

durch eine unangemessene Entsorgung dieses Produkts entstehen könnten. Genauere Informationen zur Wiederverwertung dieses Produkts erhalten Sie von Ihrer Stadtverwaltung, der Müllabfuhr vor Ort oder dem Geschäft, in dem Sie dieses Produkt erworben haben.

Français

Le symbole sur le produit ou sur son emballage indique que ce produit ne doit pas être traité comme un déchet ménager. Il doit au contraire être remis au point de collecte correspondant pour le recyclage du matériel électrique et électronique. En procédant de cette manière, vous aiderez à prévenir les conséquences  otentiellement négatives pour l’environnement et la santé humaine que pourrait causer un traitement inadéquat du rejet de ce produit . Pour plus ample information sur le recyclage de ce produit, veuillez prendre contact avec

votre bureau municipal, votre service de collecte de déchets ménagers ou le magasin où vous avez acheté le produit.

Português

Símbolo no produto ou na embalagem indica que

esse produto não deve ser tratado como um resíduo doméstico. Ao contrário, deve ser levado ao local de recolha adequado para a reciclagem de equipamentos electroelectrónicos. Ao se assegurar que o tratamento deste equipamento foi adequado, estará a ajudar a prevenir consequências potenciais ao meio ambiente e à saúde humana que poderiam ser causadas pelo manejo inapropriado do produto. Para mais informações sobre a reciclagem deste produto, entre em contacto com as autoridades locais, com o órgão responsável pela recolha de lixo ou a loja onde o produto foi adquirido.

Italiano

Il simbolo sul prodotto o sulla confezione indica che questo prodotto non può essere smaltito fra i rifiuti domestici. Deve invece essere consegnato a un centro di raccolta autorizzato per il riciclaggio dei dispositivi elettrici ed elettronici. Smaltendo questo prodotto in modo corretto, si contribuisce a ridurre l’impatto ambientale e sull’uomo. Per maggiori informazioni sul riciclaggio di questo prodotto, contattare il proprio comune, il centro di raccolta dei rifiuti urbani locale o il rivenditore.

Nederlands

Het symbool	op het product of de verpakking geeft aan dat dit product niet als huishoudelijk afval mag worden behandeld. Het apparaat moet bij een verzamelpunt voor het recyclen van elektrische en elektronische apparatuur worden ingeleverd. Door dit product op de juiste manier af te danken, helpt u bij het voorkomen van mogelijke negatieve consequenties voor het milieu en de menselijke gezondheid. Deze zouden kunnen ontstaan als dit product niet op de juiste manier wordt behandeld. Voor uitgebreide informatie over het

recyclen van dit product kunt u contact opnemen met uw plaatselijke stadskantoor, uw afvalverwerkingsdienst of de winkel waar u het product hebt gekocht.

Español

El símbolo que aparece en el producto o en su embalaje indica que este producto no puede ser tratado como residuo doméstico. En su lugar, debe ser entregado en el correspondiente punto de recogidapara el reciclado de equipos eléctricos y electrónicos. Al garantizar la adecuada eliminación de este producto, ayudará a evitar las posibles consecuencias negativas para el medio ambiente y la salud de las personas quese producirían a causa de una inadecuada manipulación de los residuos de este producto. Para obtener información más detallada acerca del reciclaje de este producto, póngase en contacto con la oficina local de su ciudad, el servicio de recogida de residuos domésticos oel establecimiento en el que ha adquirido el producto.

Svenska

Symbolen på produkten eller emballaget anger att produkten inte får hanteras som hushållsavfall. Den skall i stället lämnas in på uppsamlingsplats för återvinning av el- och elektronikkomponenter. Genom att säkerställa att produkten hanteras på rätt sätt bidrar du till att förebygga eventuellt negativa miljö- och hälsoeffekter som kan uppstå om produkten kasseras som vanligt avfall. För ytteligare upplysningar om återvinning bör du kontakta lokala myndigheter, sophämtningstjänst eller affären där du köpte varan.

Dansk

Symbolet, som findes på produktet eller emballagen, viser, at produktet ikke må bortskaffes sammen med almindeligt husholdningsaffald. Det skal derimod afleveres på en miljøstation, som er godkendt til håndtering af elektrisk og elektronisk udstyr. Sørg for at bortskaffe produktet korrekt, så du kan være med til at forebygge skader på miljøet og menneskers sundhed.  Hvis du ønsker yderligere oplysninger om, hvordan produktet genvindes, kan du henvende dig hos kommunen, en miljøstation eller forretningen, hvor du købte produktet.

Suomi

Tuotteessa tai pakkauksessa oleva symboli  ilmaisee, että tuotetta ei voi hävittää talousjätteen  mukana. Sen  sijaan tuote on vietävä sähköisten ja  elektronisten laitteiden kierrätykseen tarkoitettuun  keräyspisteeseen. Kun huolehdit tuotteen asianmukaisesta hävittämisestä, autat edistämään ympäristön  ja ihmisten hyvinvointia, jonka tuotteen virheellinen  hävittäminen voi vaarantaa. Lisätietoa tämän tuotteen  kierrättämisestä saat jätteenkäsittelypisteistä tai  samasta liikkeestä, josta ostit tuotteen.

Norsk

Symbolet på produktet eller emballasjen  indikerer at dette produktet ikke kan behandles som  husholdningsavfall. I stedet skal det leveres til aktuelt innsamlingspunkt for resirkulering av elektrisk og elektronisk utstyr. Ved å sørge for at dette produktet kasseres korekt, bidrar du til å forebygge mulige  negative følger for miljøet og folks helse, hvilket ellers  kan forårsakes ved feilaktig avfallshåndtering av dette produktet. For nærmere informasjon om resirkulering av dette produktet, vennligst kontakt din lokale  representant, renholdsverket eller butikken der du  kjøpte produktet.

Chapter		     Page

1. General safety instructions	5

2. First time instructions	9

3. Operating instructions	10

4. Transport	13

5. Storage	13

6. Environmental protection	14

7. Maintenance, cleaning, repair	14

8. Trouble shooting	15

| Rated Pressure | 110 bar /11 MPa |
| --- | --- |
| Max. pressure | 165 bar / 16.5MPa |
| Flow | 5.5 l/min |
| Power | 2200W |
| Voltage | 230V~50Hz |
| Vibration gun | Max 2.25 m/s2 |
| Maximum temperature of water | 60℃ |

- Water inlet coupling

- Electrical plug

- Storage hook

- Water outlet

- Switch

- Trolley handle

- Detergent tank

- Cable hook

- Wheel

- High pressure hose

- Trigger gun

- Trigger lock

- Hose reel

- Handle for hose reel

- Lance

- Multi Nozzle

- Detergent spray nozzle

- Turbo Nozzle

- Brush

- Patio Cleaner

21. Rotary Brush

22. Adapter for Brush

23. Adapter for Gun

Read all  safety  warnings  and instructions. Failure to heed warnings and follow instructions may result in electric shock, fire and/or serious injury. Keep safety warnings and instructions for future reference. The term "power tool" in the safety warnings refers to your mains operated

(corded) power tool or battery-operated (cordless) power tool.

SYMBOLS

The following symbols are used in this manual and/or on the machine:

|  | The jet must not be directed at persons, pets, live electrical equipment or the appliance itself. |
| --- | --- |
|  | In accordance with essential safety standards of applicable European directives |
|  | Class II - The machine is double insulated; Earthing wire is therefore not necessary. |
|  | Read manual before use |
|  | Denotes risk of personal injury or damage to the tool. |
|  | Wear gloves |
|  | Wearing of protection against noise advised |
|  | Wearing eye protection is advised |
|  | Acoustic power level |

Working area

● Keep working area clean and well lit. Untidy and dark areas can lead to accidents.

● Do not operate power tools in potentially explosive surroundings, for example, in the

presence of inflammable liquids, gases or dust. Power tools create sparks which may ignite

the dust or fumes.

● Keep children and bystanders at a distance when operating a power tool. Distractions can

cause you to lose control of it.

Electrical safety

Always check that the power supply corresponds to the voltage on the

rating plate.

● Power tool plugs must match the outlet. Never modify the plug in any way. Do not use adapter plugs with earthed power tools. Unmodified plugs and matching outlets will reduce the risk of a lethal electric shock.

● Avoid body contact with earthed surfaces such as pipes, radiators, kitchen ranges and refrigerators. There is an increased risk of a lethal electric shock if your body is earthed .

●  Do not expose power tools to rain or wet conditions. If water gets inside a power tool, it will increase the risk of a lethal electric shock.

●  Do not damage the cord. Never use the cord for carrying, pulling or unplugging the power tool. Keep the cord away from heat, oil, sharp edges or moving parts. Damaged or entangled cords increase the risk of a lethal electric shock.

● When operating a power tool outdoors, use an extension cable suitable for outdoor use.

● Using a cord suitable for outdoor use reduces the risk of a lethal electric shock.

● If operating a power tool in a damp location is unavoidable, use a power supply protected

by a residual current device (RCD). Using an RCD reduces the risk of a lethal electric

shock.

Personal safety

● Stay alert, watch what you are doing and use common sense when operating a power tool.

Do not use a power tool when you are tired or under the influence of drugs, alcohol or medication. A moment of inattention when operating a power tool may result in serious

personal injury.

● Use safety equipment. Always wear eye protection. Using safety equipment such as a dust mask, non-skid safety shoes, a hard hat, or hearing protection whenever it is needed will reduce the risk of personal injury.

● Avoid accidental starts. Ensure the switch is in the off position before inserting the plug.

Carrying power tools with your finger on the switch or plugging in power tools when the switch is in the on position makes accidents more likely.

● Remove any adjusting keys or spanners before turning on the power tool. A spanner or key left attached to a rotating part of the power tool may result in personal injury.

● Do not reach out too far. Keep your feet firmly on the ground at all times. This will enable you retain control over the power tool in unexpected situations.

● Dress properly. Do not wear loose clothing or jewellery. Keep your hair, clothing and gloves away from the power tool. Loose clothes, jewellery or long hair can become entangled in the moving parts.

● If there are devices for connecting dust extraction and collection facilities, please ensure that they are attached and used correctly. Using such devices can reduce dust-related

hazards.

Risk of explosion!

Do not spray flammable liquids.

Never draw in fluids containing solvents

or undiluted acids and solvents! This includes petrol, paint thinner and heating

oil. The spray mist thus generated is highly

inflammable, explosive and poisonous.

Do not use acetone, undiluted acids and

solvents as they are damaging to the materials from which the appliance is made.

Power tool use and care

● Do not expect the power tool to do more than it can. Use the correct power tool for what you want to do. A power tool will achieve better results and be safer if used in the context

for which it was designed.

● Do not use the power tool if the switch cannot turn it on and off. A power tool with a broken switch is dangerous and must be repaired.

● Disconnect the plug from the power source before making adjustments, changing accessories, or storing power tools. Such preventive safety measures reduce the risk of starting the power tool accidentally.

● Store power tools, when not in use, out of the reach of children and do not allow people who are not familiar with the power tool or these instructions to operate it. Power tools are potentially dangerous in the hands of untrained users.

● Maintenance. Check for isalignment or jammed moving parts, breakages or any other feature that might affect the operation of the power tool. If it is damaged, the power tool must be repaired. Many accidents are caused by using poorly maintained power tools.

● Keep cutting tools sharp and clean. Properly maintained cutting tools with sharp cutting

edges are less likely to jam and are easier to control.

● Use the power tool, accessories and cutting tools, etc., in accordance with these instructions and in the manner intended for the particular type of power tool, taking into account the working conditions and the work which needs to be done. Using a power tool

in ways for which it was not intended can lead to potentially hazardous situations.

Service

●  Your power tool should be serviced by a qualified specialist using only standard spare parts. This will ensure that it meets the required safety standards.

Danger

Turn off the appliance and remove the

mains plug prior to any care and maintenance work.

Repair works may only be performed by the authorized customer service.

ADDITIONAL SAFETY INSTRUCTIONS FOR HIGH-PRESSURE

CLEANERS

● The appliance is designed solely for outdoor private use and NOT for commercial use.

Please keep it away from heat, direct sunlight, moisture and rain, frost and sharp edges.

●High-pressure hoses, fixtures and couplings are important for the safety of the appliance. Only use high-pressure hoses,

fixtures and couplings recommended by the manufacturer.

●This appliance is not intended for use

by persons with reduced physical, sensory

or mental capabilities.

The appliance must not be operated by

children or persons who have not been

instructed accordingly.

Children should be supervised to prevent

them from playing with the appliance.

Keep packaging film away from children

- risk of suffocation!

● Do not let people who have not been trained in the use of a high pressure washer nor read the instruction manual operate the machine!

● High pressure cleaners shall not be used by children or untrained personnel.

● Children should be supervised to ensure that they do not play with the appliance.

● Before starting up your machine please check it carefully for any defects. If you find any, do not start up your machine and contact your local distributor.

● Check especially the insulation of the electric cable should be faultless and without any cracks. If the electric cable is damaged, an authorized local service centre should replace it.

WARNING: High pressure jets can be dangerous if subject to misuse. The

jet must not be directed at persons, live electrical equipment or the

appliance itself.

WARNING: Do not use the appliance within range of persons unless they

wear protective clothing.

● Do not direct the jet against yourself or others in order to clean clothes or foot-wear.

● old the spray lance firmly with both hands.

● The operator and anyone in the immediate vicinity of the site of cleaning should take action

to protect them from being struck by debris dislodged during operation.

● Wear goggles and protection clothes during operation.

WARNING: This appliance has been designed for use with the cleaning

agent supplied or recommended by the manufacturer. The use of other

cleaning agents or chemicals may adversely affect the safety of the

appliance.

● Disconnect from electrical power supply before carrying out user maintenance.

● To ensure appliance safety, use only original spare parts from the manufacturer or approved by the manufacturer.

● Do not use the appliance if a supply cord or important parts of appliance are damaged, e.g. safety device, high pressure hose and trigger gun.

● Do not use the appliance with wet hands. If the appliance is humid or wet, unplug it immediately. Do not put it in water.

● Tires and tire valves may be damaged by the high-pressure jet and then burst.

●  Never use the machine in an environment where there could be a danger of explosion.

●  It is not allowed to clean asbestos- containing surfaces with high pressure.

●  This high pressure washer must not be used at temperatures below 0°C

WARNING: High pressure hoses, fittings and couplings are important for the safety of the appliance. Use only hoses, fittings and couplings

recommended by the manufacturer.

WARNING: Inadequate extension cables can be dangerous. Cables on reels should always be completely unwinded to prevent the cable from

overheating.

WARNING: Inadequate extension cords can be dangerous.

●  If an extension cable is used, the plug and the socket must be waterproof and comply with the below-mentioned requirements for length and cable dimensions.

- 1.0 mm² max. 12.5 m

- 1.5 mm² max. 20 m

●  If the electric cable is damaged, it must be replaced by the manufacturer or his service

agent or similarly qualified person in order to avoid a hazard.

MAINS POWER CONNECTION

The following should be observed when connecting the high pressure washer to the electric installation:

● The electric supply connection shall be made by a qualified electrician and comply with IEC 60364-1

● It is recommended that the electric supply to this appliance should include either a residual current device that will interrupt the supply if the leakage current to earth exceeds 30 mA for 30 ms.

WATER CONNECTION

● Connection to the public mains according to regulations.

●  Inlet hose can be connected to the water mains with a max. inlet pressure of 10 bars.

The appliance is not intended to be connected to a water supply. This high-pressure cleaner can be connected (only in Europe) a potable water system when an appropriate backflow network has been installed, type BA according to EN 1717. The length of the pipe between the backflow preventer and the high-pressure cleaner must be at least 10 meters to absorb pressure peaks possible (minimum diameter 1.27 cm)

As soon as water has flown through the BA valve, this water is not considered to be drinking water any more.

IMPORTANT!

Only use water without any impurities. If there is a risk of sand particles in the inlet water (i.e. from your own well), an additional filter should be mounted.

SAFETY DEVICES

● The unloader valve can reduce pressure if it exceeds pre-set values.

Locking device on trigger gun (12) (see illustration at the beginning of this manual): The trigger gun (11) features a locking device (12). When the knob is activated, the trigger gun (11) cannot be operated.

CAUTION

Prior to cleaning, make sure that the high pressure is placed safely on level ground.

Wear protective goggles and protective

clothing during the cleaning process.

DANGER

The trigger gun is subjected to a recoil force when the water jet is discharged. Make sure that you have a firm footing and are also holding the trigger gun and spray lance firmly.

THERMAL SENSOR

A thermal sensor protects the motor against overloading. The machine will restart after a few minutes when the thermal sensor has cooled.

NOISE

Noise values measured according to relevant standard:

● Acoustic pressure level accord to the standard EN60335-2-79 : LpA= 78 dB(A)  K=3 dB(A)

● Acoustic power level accord to the standard accord to the standard EN60335-2-79 :LwA= 95 dB(A)

This section will explain in details how to make you high pressure washer ready for use.

Slide the storage hooks (3) into the holders.

Slide the cable hooks (8) into the holders.

- Insert the extension lance into to the housing

- Fix the extension lance with the  two screws to the housing

- Insert the rotor arm into the extension lance

- Insert the U-pin to fix the rotor arm. NOTE: Make sure the rotor arm is properly fixed to the extension lance with the U-pin

- Screw the water inlet coupling (1) tight on to the water inlet Note: The inlet filter (A) must always be fitted in the water inlet pipe to filter out sand, lime stone and other impurities as these will damage the pump valves. Caution: Failure to fit the filter will invalidate the guarantee.

- Connect the garden hose with a standard quick coupling.

- Attach the high pressure hose (10) to the trigger gun (11) and machine.

Detach the high pressure hose by pressing the pawl (B) or button (C)

- Push the lance (15) into the trigger gun (11)

- When inserted turn it. Caution: Make sure the lance (15) is properly fixed to the gun (11)

- Attach the nozzles (16-21). Caution: When attaching the nozzle (16-21) the button (D) on the nozzle (16-21) should come out again. Check before activating the trigger that the nozzle (16-21) is properly fixed.

An ordinary 1/2" garden hose of min. 10 m and max. 25 m will be suitable.

IMPORTANT! Only use water without any impurities. If there is a risk of sand particles in the inlet water (i.e. from your own well), an additional filter should be mounted.

- Let the water run through the water hose before connecting it to the machine to prevent sand and dirt from penetrating the machine. Note: Check that the filter is fitted in the water inlet pipe and that it is not clogged up.

- Connect the water hose to the water supply by means of the quick connector (inlet water, max. pressure: 10 bar, max. temperature: 60°C).

- Turn on the water.

The trigger gun (11) and lance (15) is affected by a thrust during operation - therefore always hold it firmly with both hands.

IMPORTANT: Point the nozzle at the ground.

- Check that the machine is in upright position. NOTE: Do not place the machine in high grass!

- Release the trigger lock (12)

- Activate the trigger of the trigger gun (11) and let the water run until all air has escaped from the water hose.

- Press the Start/stop switch (5).

- Activate the trigger of the trigger gun (11).

- Always adjust the distance and thus the pressure of the nozzle to the surface, which is to be cleaned.

Do not cover the machine during operation or use it in a room without adequate ventilation!

NOTE: If the machine is left or not used for 5 minutes, it must be switched off on the start/stop switch (5) "O":

- Press the start/stop switch (5) "O".

- Disconnect the electrical plug (2) from the socket.

- Shut off the water supply and activate the trigger of the trigger gun (11) to relieve the machine of pressure.

- Lock the trigger gun (11)

When releasing the trigger of the trigger gun (11), the machine automatically stops. The machine will start again when you re- activate the trigger gun (11)

The pressure can for the multi nozzle (16) be adjusted by tuning it.

WARNING: Do not do this under operation to avoid that the hand hits the jet.

- Unscrew the lid of detergent tank(7)

- Add detergent to detegent tank(7)

- Attach the detergent spray nozzle(17) to gun lance(15).

NOTE: Use detergnt spray nozzle to spray detergent when you want to use detergent from the detergent tank.

The trigger gun (11) and lance (15) can be stored during and after operation in the storage hook(3)

The hose reel (13) is used for storage of the hose. Use the handle (14) to crank in the hose.

WARNING: Do not use the hose reel (13) when the high pressure hose is under pressure. This will damage the sealings and this is not covered by the warranty.

The angle nozzle (19) can be used for many applications e.g cleaning the underbody of a car , underneath a lawn mover without being splashed back with debris, etc

After attaching the angle nozzle (19) be aware of the moment on the lance trigger gun (11) and lance (15) as the jet is coming out perpendicular to these.

The patio cleaner is a powerful accessory for cleaning patio, driveways, etc.

Attach the Patio Cleaner (21) to the lance (15).

NOTE: Do not use the Patio Cleaner (21) as a broom but let is surf smoothly over the surface

● Release the lever on the trigger gun.

● Lock the lever on the trigger gun.

● During longer breaks (more than 5 minutes), also turn the appliance off using the "0/OFF" switch.

● Insert the trigger gun in its holder.

Caution

In order to prevent accidents or injuries, keep in mind the weight of the appliance during transport

Illustration!

● To push the appliance, the transport handle must be pulled all the way up; it will lock into place audibly.

● Pull the appliance by its transport handle.

● Lift appliance by the carrying handle and carry it.

● Secure the appliance against shifting

and tipping over.

The machine should be stored in a frost-free room!

Pump, hose and accessories should always be emptied of water prior to storing as follows:

- Stop the machine (press the start/stop switch (5) “O” and detach water hose, high pressure hose (10) and nozzle (16-21)

- Restart the machine (5) and activate the trigger of the trigger gun (11). Let the machine run until no more water runs through the trigger gun (11)

- Stop the machine, unplug and wind up hose and cable.

- Place trigger gun (11), lance (15), nozzles(16-21) and other accessories in the holders of the machine. The hook (3) can be used for storage of the hose (10) and cord (2)

Should the machine by mistake be frozen, it will be necessary to check it for damage.

WARNING: Never start up a frozen machine. Frost damages are not covered by the guarantee!

Old appliances contain valuable materials that can be recycled. Please arrange for the proper recycling of old appliances. Please dispose your old appliances using appropriate collection systems.

WARNING! Always disconnect the electrical plug from the socket prior to maintenance or cleaning.

To ensure a long and problem free working life, please take the following advice:

- Wash out water hose, high pressure hose, spray lance and accessories before mounting

- Clean the connectors of dust and sand.

- Rinse the detergent spraying attachment after use.

- Clean the nozzles.

Any repair should always be made in an authorized workshop with original spare parts

Clean the water inlet filter regularly once a month or more frequently according to use.

Carefully loosen the filter with a screwdriver and clean it (see section 3.1). Check that it is intact before re-mounting it.

The inlet filter must always be fitted inside the water inlet pipe to filter out sand, limestone and other impurities, as they will damage the pump valves.

CAUTION: Failure to fit the filter will invalidate the warranty

The machine should be kept clean so as to let cooling air pass freely through the machine vents.

To ensure an easy connection and that o-rings do not dry up; the couplings should be greased regularly.

| Symptom | Cause | Recommended action |
| --- | --- | --- |
| Machine refuses to start | Machine not plugged in | Plug in machine. |
|  | Defective socket | Try another socket. |
|  | Fuse has blown | Replace fuse. Switch off other machines. |
|  | Defective extension cable | Try without the extension cable. |
| Fluctuating pressure | Pump is sucking air | Check that hoses and connections are airtight. |
|  | Valves dirty, worn out or stuck | Contact your nearest service centre |
|  | Water supply not sufficient | Increase water pressure, check for blockage of garden hose and/or change to bigger hose. |
|  | Pump seals worn | Contact your nearest service centre |
| Machine stops | Fuse has blown | Replace fuse. Switch off other machines. |
|  | Incorrect mains voltage | Check that the mains voltage corresponds to specification on the name plate |
|  | Thermal sensor activated | Leave the machine for 5 minutes to cool down |
|  | Nozzle partially blocked | Clean the nozzle with a needle and by spraying water backwards through the nozzle |
| Fuse blows | Fuse too small | Change to an installation higher than the amperage consumption of the machine. |
|  | Amperage increase | Try without the extension cable. |
| Machine pulsating | Air in inlet hose/pump | Allow machine to run with open trigger until regular working pressure resumes. |
|  | Inadequate supply of mains water specifications required | Increase water pressure, check for blockage of garden hose and/or change to bigger hose. |
|  | Nozzle partially blocked | Clean the nozzle with a needle and by spraying water backwards through the nozzle |
|  | Water filter blocked | Clean the filter |
|  | Hose kinked | Straighten out hose. |
| Machine often starts and stops by itself | Pump and/or trigger gun is leaking | Contact your nearest service centre |
|  | No water supply | Connect inlet water. |
| Machine starts but no water comes out | Water filter blocked | Clean the filter |
|  | Nozzle blocked | Clean the nozzle with a needle and by spraying water backwards through the nozzle |

# Text boxes

Zhejiang xinchang bigyao Power Tool Co., Ltd.

WARNING: Do not use the appliance without reading the instruction manual.

WEEE - Waste of Electric and Electronic Equipment

WEEE - Waste of Electric and Electronic Equipment

EN

Content

Technical Data

Circuit Diagram

Product Overview

1. General safety instructions

EN

EN

EN

EN

EN

2. First time instructions

EN

2.1Mounting of storage hook

2.2Mounting of cable hook

2.3 Mounting of Patio Cleaner (optional)

4

2

3

1

3. Operation instructions

3.1 Connection of garden hose

A

1

EN

3.2 Mounting of high pressure hose

B

C

3.3 Mounting of lance and nozzle

2

D

1

3

3.4 Water connection

3.5 Start/stop of the machine

EN

3.6 Multi Nozzle

3.7 Use of detergent

7

3.8 Storage hook

3.9 Hose reel

13

14

3.10Angle Nozzle (optional)

3.11 Patio Cleaner (optional)

3. 12 Interrupting operation

4. Transport

4.1 When transporting by hand

4. 2 When transporting in vehicles

5. Storage

EN

6. Environmental protection

7. Maintenance, cleaner and repair

EN

7.1 Cleaning of inlet filter

7.2 Cleaning of air vents

7.3 Greasing of couplings

8. Trouble shooting

EN