ORIGINAL INSTRUCTIONS

RIDE-ON LAWN MOWER

Model : RAC6196PR-1

WARNING: Please read all instructions carefully before operating the machine!

BUILDER SAS

32, rue Aristide Bergès - ZI 31270 Cugnaux – France

Made in PRC

Dear Customer,

Thank you for having chosen one of our products. We hope that you will get complete satisfaction from using your new machine and that it will fully meet all your expectations. This manual has been compiled in order that you may get to know your machine and to be able to use it safely and efficiently. Don’t forget that it forms an integral part of the machine, so keep it handy so that it can be consulted at any time and pass it on to the purchaser if you resell the machine.

This new machine of yours has been designed and made in line with current regulations, and is safe and reliable if used for cutting and collecting grass according to the instructions given in this manual (proper usage). Using the machine in any other way or ignoring the instructions for safe usage, maintenance and repair is considered "incorrect usage" （☛5.1）which will invalidate the guarantee and the manufacturer will decline all responsibility, placing the blame with the user for any damage or injury to himself or others in such cases.

Since the product is continually being improved, you may find slight differences between your machine and the descriptions contained in this manual. Certain modifications can be made to the machine without prior warning and without the obligation to update the manual, although the essential safety and function characteristics will remain unaltered. In case of any doubts, do not hesitate to contact your Retailer. And now enjoy your work!

This manual gives all the necessary instructions for using the machine and the basic maintenance that may be carried out by the user.

For any information not contained here, contact your Local Retailer or a Licensed Service Centre.

If you wish, your Retailer will be pleased to offer maintenance programmed personalized to your needs. This will enable you to keep your new acquisition in peak performance, maintaining its value.

1. SAFETY ........................................................................................................................4

2. IDENTIFICATION OF THE MACHINE AND COMPONENTS.......................................9

3. UNPACKING AND ASSEMBLY .................................................................................10

4. CONTROLS AND INSTRUMENTS .............................................................................12

5. HOW TO USE THE MACHINE ....................................................................................16

6. MAINTENANCE .......................................................................................................... 26

7. ENVIRONMENTAL PROTECTION ............................................................................ 30

8. TROUBLESHOOTING................................................................................................ 31

9. ACCESSORIES ON REQUEST ................................................................................. 33

10. SPECIFICATIONS .................................................................................................... 34

11. DECLARATION OF CONFORMITY ..........................................................................35

12. WARRANTY ............................................................................................................. 36

13. PRODUCT FAILURE  ..............................................................................................37

14. WARRANTY EXCLUSIONS ..................................................................................... 38

1.1 HOW TO READ THE MANUAL

This manual describes various versions of the machine, which mainly differ in:

– type of transmission: with either mechanical gear change or continuous speed converter.

– the inclusion of components or accessories which may not be available in some areas;

– special equipment fitted.

The symbol  highlights all the differences in usage and is followed by the indication of the version that it refers to.

The symbol “☛ ” makes a reference to another part of the manual where further information or clarification can be found.

Some paragraphs in the manual containing information of particular importance for safety and operation are highlighted and signify the following:

These give details or further information on what has already been said, and aim to prevent damage to the machine.

Non-observance will result in the risk of injury to oneself

or others.

Non-observance will result in the risk of serious injury or death to oneself or others                                                                                                                                                                                        Whenever a reference is made to a

position on the machine “front”, “back”, “left” or “right” side, this

is determined by facing the direction of forward travel.

For all usage and maintenance

operations on the engine or the battery which are not described

in this manual, consult the relevant manuals which form an integral

part of all the documentation supplied with the machine.

1.2 GENERAL SAFETY REGULATIONS

Read carefully before using the machine.

A) TRAINING

1) Read the instructions carefully. Be familiar with the controls and how to use the

equipment properly.

2) Never let children or people unfamiliar with these instructions use the machine. Local

regulations can restrict the age of the user.

3) Never mow while people, especially children, or pets are nearby.

4) Keep in mind that the operator or user is responsible for accidents or hazards occurring

to other people or their property.

5) Do not carry passengers.

6) All drivers should seek and obtain professional and practical instruction. Such

instruction should emphasize:

– the need for care and concentration when working with ride on machines;

– you cannot use the brake to regain control of a ride-on machine sliding down a slope. The main reasons for loss of control are:

– insufficient wheel grip;

– over speeding;

– inadequate braking;

– the type of machine is unsuitable for its task;

– unawareness of the effect of ground conditions, especially slopes;

B) PREPARATION

1) While mowing, always wear sturdy footwear and long trousers. Do not operate the equipment barefoot or wearing open sandals.

2) Thoroughly inspect the area where the equipment is to be used and remove all objects which can be ejected from the machine.

3) DANGER! Petrol is highly flammable:

– store fuel in containers specifically designed for this purpose;

– refuel outdoors only and do not smoke while refueling;

– add fuel before starting the engine. Never remove the cap of the fuel tank or add petrol while the engine is running or when the engine is hot;

– if you spill petrol, do not start the engine and move the machine away from the area of

spillage. Do not create any source of ignition until the petrol vapors have evaporated;

– put back and tighten all fuel tank and container caps securely.

4) Replace faulty silencers.

5) Before use, always visually inspect to see that the blade, blade bolts and cutter assembly are not worn or damaged. Replace the worn or damaged blade and bolts in sets

to preserve the balance.

C) OPERATION

1) Do not start the engine in a confined space where dangerous carbon monoxide fumes can collect.

2) Mow only in daylight or good artificial light.

3) Before starting the engine, disengage the blades and shift into neutral.

4) Do not use on slopes of more than 10° (17%).

5) Remember there is no such thing as a “safe” slope.

Travelling on grass slopes requires particular care. To guard against overturning:

– do not stop or start suddenly when going up or downhill;

– engage the drive slowly and always keep the machine in gear, especially when travelling downhill;

– machine speeds should be kept low on slopes and during tight turns;

– stay alert for humps and hollows and other hidden hazards;

– never mow across the face of the slope.

6) Stop the blade from rotating before crossing surfaces other than grass.

7) Never use the machine with damaged guards, or without the safety protective devices in place.

8) Do not change the engine governor settings or over speed the engine. Operating the engine at excessive speed can increase the risk of personal injury.

9) Before leaving the driving seat:

– disengage the blades and lower the attachments;

– go into neutral and apply the parking brake;

– stop the engine and remove the ignition key (in the electric start models).

10) Disengage the blade, stop the engine and remove the ignition key (in the electric start models):

– before clearing blockages or unclogging chutes;

– before cleaning, checking or working on the machine;

– after striking a foreign object. Inspect the machine for any damage and make repairs before restarting and operating the equipment;

– If the machine starts to vibrate abnormally (inspect it immediately).

11) Disengage the blade when transporting or whenever it is not in use.

12) Stop the engine and disengage the blade:

– before refueling;

– before removing the grass-catcher.

13) Reduce the throttle setting before stopping the engine.

D) MAINTENANCE AND STORAGE

1) Keep all nuts, bolts and screws tight to be sure the equipment is in safe working condition.

2) Never store the equipment with petrol in the tank inside a building where fumes may reach an open flame or spark.

3) Allow the engine to cool before storing in any enclosure.

4) To reduce fire hazards, keep the engine, silencer, battery compartment and petrol storage area free of grass, leaves, or excessive grease.

5) Check the grass-catcher frequently for wear or deterioration.

6) Replace worn or damaged parts for safety purposes.

7) If the fuel tank has to be drained, this should be done outdoors.

8) When the machine is to be stored or left unattended, lower the cutting deck.

Improper maintenance can reduce life of the tool and create accident and damages. Always bring maintenance.

the lawnmower safety systems or features shall not be tampered with or disabled;

the operator should not alter or tamper with any sealed adjustments for the engine speed control;

Warning: there is a danger of moving blade assemblies during adjustment;

Use the tool only for the intended use as described in manual. Misuse will create accidents and damages.

Warning: do not use the tool while being tired, ill or under influence of alcohol or other drugs.

The lawnmower shall not be operated without either the entire grass catcher or self-closing discharge opening guard in place”

It misses instructions regarding exposure to noise, selection and use of hearing protection, including recommendations for limiting the duration of operation,

Prolonged use will expose the user to vibration which can affect health. Limit the duration of operation and wear gloves.

Warning: Do not use of the lawnmower when there is a risk for lightning;

Residual risks

Even if you use this product in compliance with all safety requirements, the potential risks of injury and damage remain. The following hazards may arise in the structure and design of this product:

Always be vigilant when using this product, so you can recognize and manage the risks rather.

There are adverse health consequences resulting from the emission of vibration if the product is used for long periods of time or not properly managed and properly maintained.

There are risks of injury and property damage due to attachments or broken the sudden impact of hidden objects when using cutting.

Risk of injury to persons and property caused by flying objects.

Prolonged use of this product exposes the operator to vibrations and can produce so-called "white finger" disease. To reduce the risk, wear gloves and keep your hands warm.

If any of the symptoms of "white finger syndrome" occur, seek immediate medical attention.

Symptoms of "white finger" include numbness, loss of sensitivity, tingling, tingling, and pain, loss of strength, color changes or skin condition. These symptoms usually appear on the fingers, hands or wrists. Risk increases at low temperatures.

There is a risk of loss hearing in case of prolonged use and when a hearing protection is not worn. Wear hearing protection.

Intended use

This model of thermal mower is designed for natural grass mowing. Any other use is prohibited.

It is suitable only for private use in a garden or plot. Lawnmowers designed for private plots or gardens are those used for the maintenance of grassy areas and private lawns and should not be used in public areas, parks, sports, agricultural or forest areas.

1.3 SAFETY LABELS

Your machine must be used with care. Therefore, labels have been placed on the machine to remind you pictorially of the main precautions to take during use. These labels are to be considered an integral part of the machine. If a label should fall off or become illegible, contact your Retailer to replace it. Their meaning is explained below.

Warning: Read the Operator’s Manual before operating this machine.                                                                                                  Warning (in the manual start models): disconnect the spark plug cap

and read the instructions before carrying out any maintenance or repairs.

Warning (in the electric start models): remove the key and read the instructions before carrying out any maintenance or repairs.

Danger! Ejected objects: Keep bystanders away.

Danger! Dismemberment: Make sure that children stay clear of the machine all the time when engine is running.

Danger! Ejected objects: Do not operate without the grass

catcher in place.

Danger! Machine rollover: Do not use this machine on slopes

greater then 10°

Danger of cutting yourself. Blade in movement. Do not put hands or feet near or under the opening of the cutting plate.

Danger! Away from the danger of combustible substances

Danger! Do not near the operational machine

WARNING! Do not put hands or feet near rotating parts or under the cutting deck. Contact with the blade(s) can amputate hands and feet.

Danger ! Electrical shock !

This symbol indicates the surface is very hot and not touching

Guaranteed sound power level

2.1 NAME AND ADDRESS OF MANUFACTURER

The machine is composed of a series of main component                                                                                                                                                 11. Cutting deck: this is the guard enclosing the rotating blade

12. Blade: this is what cuts the grass. The wings at the ends help convey the cut grass towards the collector channel.

13.Side discharge: as well as collecting the grass cuttings, this is also a safety element in that it stops any objects drawn up by the blade from being thrown outside of the machine.

14. Engine: this moves the blade and drives the wheels. Its specifications and regulations for use are described in a specific manual.

15. Batteries (only in the electric start models): provides the energy for starting the engine. Its specifications and regulations for use are described in a specific manual.

16. Driver seat: this is where the machine operator sits. It has a sensor which detects the presence of the operator and acts as a safety device.

17. Labels for regulations and safety: give reminders on the main provisions for working safely, each of which is explained in chapter 1.

18. Engine cover: for access to the engine

For storage and transport purposes, some components of the machine are not installed in the factory and have to be assembled after unpacking. Follow the instructions below.                                                                                                The machine is supplied without engine oil or fuel. Before starting the engine, fill with oil and fuel following the instructions given in the engine manual.

Unpacking and completing the assembly should be done on a flat and stable surface, with enough space for machine handling and its   packaging, always making use of suitable equipment.

3.1 UNPACKING

When unpacking the machine, take care to gather all the individual parts, fittings and documentation.

To avoid damaging the cutting deck when getting the

machine down from the pallet, take it to the maximum height and be very careful.

The supply includes:

– the battery;

– bolts and screws, necessary for completing the assembly;

– a syringe for draining the engine oil.  (on request)

Disposal of the packaging should be done in accordance with the local                                regulations in force.

3.2 FITTING THE STEERING WHEEL

Place the machine on a flat surface and straighten the front wheels.

- Install steering wheel shaft (1)

- Tap in elastic cylindrical pin (2),

- Install casing (3), casing base (4),

- Align steering wheel (5) on steering wheel shaft

- Place flat washer (6) and spring washer (7) and tighten bolt (8).

3.3 FITTING THE SEAT

Fit the seat (1) onto the plate (2)

using the screws (3)

3.4 FITTING THE BLADE ENGAGEMENT LEVER

Fit the end of the lever (1) on the projecting part

of the pin (2) and fix it all by tightening the

screw (3) and nut (4)

3.5 CONNECTING THE BATTERY

1. Position the battery (1) in its compartment under the seat;

2. Connect the battery connector (2) to the machine

connector (3);                                                                                                                                                      3. Recharge the battery by following the instructions in the

Manual(☛6.2.3).

Never start the engine until the battery is fully charged!

Follow the battery manufacturer's instructions regarding safe handling and disposal.

3.6 FITTING THE SIDE DISCHARGER

a) Place the side discharge(1) on the deck (2).

b) Align the holes on deck and side discharge, then fixed them with screws(3), flat washers(4) and wing nuts(5).

c) Assembled side discharge.

4.1 STEERING WHEEL

Turns the front wheels.

4.2 CLUTCH / BRAKE PEDAL                                                                                  This pedal has a double function: during the first part of its travel it acts as a clutch, engaging and disengaging drive to the wheels, and in the second part it works the brake.

Do not keep the pedal half way of clutch engagement or disengagement, as this can cause overheating and damage the transmission belt.

When the machine is in movement, keep your foot off the pedal.

4.3 PARKING BRAKE LEVER

This lever stops the machine from moving when it has been parked.

There are two positions:

–The brake is engaged by pressing the pedal (☛4.2) right down and moving another parking lever «C» near the pedal (☛4.2) to position «B». When you take your foot off the pedal it will be blocked by the lever in the down position.

– To disengage the parking brake, press the pedal(☛4.2).The lever will return to position «A».

4.4 SPEED CHANGE LEVER

This lever has six positions for the four forward gears, the neutral position «N», and reverse «R».

- To change gear, press the pedal (☛4.2) halfway down and move the lever as per the indications on the label.

Reverse must be engaged when the machine has stopped.

4.5 CUTTING HEIGHT ADJUSTING LEVER

There are five positions for this lever, shown as «1» to «5» on the plate, which correspond to various cutting heights from 3.0 to 7.0 cm.

- To go from one position to another,

move the lever sideways and put it back in one of the stop notches.

4.6 LEVER ENGAGEMENT AND BRAKE OF BLADE

The lever has two positions, as shown on the plate:

–If the blade is engaged when safety conditions have

not been complied with, the engine shuts down and                         cannot be restarted ( ☛5.2).

– In disengaging the blade (Pos. «A»), a brake is simultaneously activated which stops their rotation within a few seconds.

4.11 KEY IGNITION SWITCH

This key operated control has three positions:

《stop》everything is switched off;

《on》  activates all parts;

《start》engages the starter

On being released at the «START» position, the key will automatically return to «ON».

4.12 ACCELERATOR LEVER

Regulates the engine's r.p.m. The positions are indicated on a plate showing the following symbols :

«CHOKE» (if fitted) = cold starting

«FAST» for maximum engine speed

«SLOW» for minimum engine speed

–The «CHOKE» position (if fitted) enriches the mixture so must only be used for the necessary time for cold starting.

– When moving from one area to another, put the lever in a position between «SLOW» and «FAST».

- When cutting, go to the «FAST» position.

4.21 PULL START HANDLE

To start the engine, take the starter cable handle and give it a firm tug.

Then put the handle back in its seat, guiding the cable as it automatically rewinds.

4.22 ACCELERATOR LEVER

It regulates the rpm and stops the engine.

The positions are indicated on the plate showing the following symbols:

«OFF» ☛4.11 for switching off the engine

«ON» ☛4.11 for switching on the engine

«CHOKE» (if fitted) = cold starting

«FAST» for maximum engine speed

«SLOW» for minimum engine speed

– When engine (for Chinese engine) start, the lever must be in a position «CHOKE».

– The «CHOKE» position (if fitted) enriches the mixture So must only be used for the necessary time for cold starting

– When moving from one area to another, put the lever in a position between «SLOW» and «FAST».

– When cutting, go to the «FAST» position.

– Disengage the blade.

– Put the lever in a P parking block.

– Hang up the grass-box

5.1 SAFETY RECOMMENDATIONS

The machine must only be used for the purpose for which it was designed (cutting and collection of grass).

Using the machine in any other way is considered "improper use" which will invalidate the warranty, relieve the manufacturer from all liabilities, and the user will

consequently be liable for all and any damage or injury to himself or others.

Examples of improper use may include, but are not limited to:

– transport people, children or animals on the machine or on a trailer;

– tow or push loads;

- use of the machine for moving over unstable, slippery, icy, stony, rough,

marshy ground and puddles that do not allow for evaluation of the consistency

of the ground;

– use of the machine for leaf or debris collection;

– use of the blades on surfaces other than grass

Do not tamper with or remove the safety devices fitted to the machine. REMEMBER THAT THE USER IS ALWAYS RESPONSIBLE FOR DAMAGE AND INJURIES TO OTHERS. Before using the machine:

– read the general safety regulations(☛1.2) , paying particular attention to

driving and cutting on slopes;

– carefully read the instructions for use, become familiar with the controls and on

how to quickly stop the blade and engine.

– never put your hands or feet next to or beneath the rotating parts and always keep away from the discharge opening.

Do not use the machine when in a precarious state of health or under the effect of medicines or other substances that can reduce your reflex actions and your ability to concentrate. It is the user's responsibility to assess the potential risk of the area where work is to be carried out, as well as to take all the necessary steps to ensure his own safety and that of others, particularly on slopes or rough, slippery and unstable ground. Do not leave the machine stopped on high grass with the engine running to avoid the risk of starting a fire. Always lower the speed when changing direction, especially on tight turns.

This machine must not be used on slopes greater than 10° (17%) (☛ 5.5).

All the references relating to the positions of controls are those described in chapter 4.

5.2 WHY THE SAFETY DEVICES CUT IN

The safety devices work in two ways:                                                                                                – by preventing the engine from starting if all the safety requirements have not been met;

– by stopping the engine if even just one of the safety requirements is lacking.

- The engine must only be started in the following conditions:

– the transmission is in “neutral”;

– the blade is not engaged;

– the operator is seated or the parking brake is engaged.

- The engine stops when:

– the operator leaves his seat when the blade is engaged;

– the operator leaves his seat with a gear engaged;

– the side discharge is lifted without disengaging the blade;

– the blade is engaged without the side discharge in place;

– the parking brake is engaged without disengaging the blade;

– the speed change is activated (☛ 4.4) with the parking brake on.

5.3 PRELIMINARY OPERATIONS BEFORE STARTING WORK

These controls ensure that the work gives the best results and is done in maximum safety.

5.3.1 Seat adjustment

Adjust the seat by sliding it along the bracket slots.

1. Loosen the four screws (1);

2. once you have found the right

position, securely tighten the four

screws (1).

5.3.2 Tire pressure

Having the correct tire pressure is essential for ensuring that the cutting deck is perfectly horizontal and thus mows evenly.

1. Unscrew the valve caps;                                                                                           2. Connect a compressed air line with a gauge to the valves and adjust the pressure to the indicated values.

3. Screw the valve caps back on.

5.3.3 Filling with oil and fuel

Refueling should be carried out in an open or well-ventilated area with engine stopped. Always remember that petrol fumes are inflammable. DO NOT TAKE A NAKED FLAME TO THE TANK’S OPENING

IN ORDERS TO SEE THE TANK’S CONTENTS AND DO NOT SMOKE WHEN REFUELLING.

The type of oil and fuel to be used is given in the engine manual.

With the engine stopped, check its oil level.

1. to reach the plug (1), remove the engine

cover (2) with the aid of a screwdriver

2. by closely following the methods described

in the engine manual, make sure the oil level is

between the MIN and MAX marks on the dipstick (3);

3. always refit the plug (1) and engine cover (2).

To refuel (to be done when the machine has stopped):

1. unscrew the plug (4) from the tank located behind the seat;

2. refuel using a funnel, but do not completely fill the tank. The tank's capacity is about 1.1 liters;

3. always refit the plug(4)

Do not drip petrol onto the

plastic parts to avoid ruining them. In the event of accidental leaks, rinse immediately with water. The warranty does not cover for damage to plastic parts of the bodywork or the engine caused by petrol.

5.3.4 Checking machine safety and efficiency

1. Check that the safety devices function as described(☛5.2).

2. Check that the brake is in perfect working order.

3. Do not start mowing if the blade vibrates or if you are unsure whether they are sharp enough. Always remember that:

– A badly sharpened blade pulls at the grass and causes the lawn to turn yellow.

– A loose blade causes unwanted vibrations and can be dangerous.

Do not use the machine if you are unsure whether it is working safely or efficiently. If in doubt, contact your Dealer immediately to make the necessary checks and repairs

5.4 USING THE MACHINE

5.4.1 Starting the engine                                                                                all starting operations have to be effected in an open or well-ventilated area! ALWAYS REMEMBER THAT EXHAUST GASES ARE TOXIC!

To start the engine:                                                                                                  1. sit on the seat and press the brake pedal right down(☛4.3);

2. put the transmission into neutral («N») (☛ 4.4);

3. disengage the blade (☛ 4.6);

4. for cold starting, put the accelerator lever in the «CHOKE» position (if fitted) as shown on the label (☛ 4.12 ). Alternatively, if the engine is still hot or without a choke, position the lever between «SLOW» and «FAST»;

5. put in the key (☛ 4.11) and turn to «ON» to make electrical contact, then turn to «START» to start the engine;

6. release the key once the engine has started;

5.take the starter cable handle (☛4.21) and firmly tug it.

6.once the engine has started, put the handle back in its seat.                                                                              7. After the machine has run for a few seconds, put the accelerator lever on        «START» and then on «SLOW».                                                                                                                                                                                                                                                                                                                    The choke (if fitted) must be closed as soon as possible. Using it when the engine is already warm can foul the spark plugs and cause the engine to run erratically.

If you have difficulty starting, do not make several attempts to avoid flooding the engine or running down the battery (if present).

– Check that the conditions allowing the engine to start are met

– Turn the key (electric start) to «OFF». Wait for a few seconds and repeat the start operation. Should the malfunction persist, refer to chapter «8» of this manual and the engine manual.

5.4.2 Starting and moving without mowing                                                                                     this machine has not been approved for use on public roads. It has to be used (as indicated by the Highway Code) in private areas closed to traffic.

When moving the machine, the blade must be disengaged and the cutting deck put at its highest position.

To start the forward movement:

1. put the accelerator control between the «SLOW» and «FAST» positions;

2.push the pedal right down (☛4.2) and put the gear change lever in 1st gear (☛4.4a).

3.release the pedal gradually to begin the movement.

Reach the desired operating speed using the accelerator and gear lever. To change gear, the clutch must always be used by pushing the pedal (☛4.2).

The pedal must be released gradually as sudden engagement may cause tipping up and loss of control of the vehicle.

Do not suddenly release the pedal and do not start moving with the gear shift more than 1/3 of the way towards «F» to avoid suddenly engaging drive which could cause the vehicle to tip and loss of control.

5.4.3 Braking

To brake:

1. first slow down the machine by reducing the engine speed;

2. push the pedal right down (☛4.2) to lower the speed even more until the

machine stops.

3. Move the speed gear shift (☛4.4) to idle «N» to permit gradual motion.

5.4.4 Retromarcia

Reverse MUST be engaged only when the machine has stopped

1.When the machine has stopped, put it in reverse by moving the lever sideways to position «R» (☛4.4);

2.gradually release the pedal to engage the clutch and then begin moving in reverse.

5.4.5 Grass cutting

The machine is not designed for heavy duty use or for mowing large quantities of grass.

The blade is engaged by means of a clutch device.

To avoid damage or premature wear of the friction elements, strictly observe the

following instructions.

To start cutting:

1. remove any foreign objects that could be hit by the blade (stones, branches, bones, wire etc.) and mark off the position of hidden elements that cannot be moved (roots, sprinklers etc.);

2. check that the grass-catcher is fitted properly;

3. put the accelerator lever into the «FAST» position;

4. bring the cutting deck to the highest position before engaging the blade;

5. only engage the blade (☛4.6) without pausing in the intermediate positions

when on the grass lawns. Avoid engaging the blade on stony ground or when

the grass is very high.

6. start moving forwards onto the grass area very gradually and with particular caution, as already described;

7. on rough ground, adjust the cutting height to prevent the blade from knocking against uneven ground or foreign objects, damaging the blade and bracket;

8.engage the most suitable gear in order to reach the desired forward speed (1st - 2nd gear)and adjust the cutting height (☛4.5) so that the quantity of grass to be removed is not too much that it jams the blade or clogs up the collector channel.

When cutting on sloping ground, the forward speed must be reduced to ensure safe conditions (☛1.2 - 5.5).

– Lower the speed whenever you note a reduction in engine speed, since a forward speed that is too fast compared to the amount of grass being cut will never mow the grass well.

– Disengage the blade and put the cutting deck in the highest position whenever you need to get past an obstacle or a hump.

–Use the 3rd gear only when moving the machine from one area to the other.

5.4.6 End of mowing

When you have finished mowing, disengage the blade, lower the engine speed and ride the machine with the cutting deck in the highest position.

5.4.7 End of work

Once you have finished mowing, stop the machine and engage the parking brake.

1. shift the accelerator lever to «SLOW»;

2. switch off the engine by turning the key to «STOP»:

Always take out the ignition key before leaving the machine unattended!

To keep the battery charged, do not leave the key in the «ON» position when the engine is not running.

1. shift the accelerator lever to «OFF».

Always make sure that the accelerator level is in the «OFF» position before leaving the machine unattended!

5.4.8 cleaning the machine

After each mowing, clean the outside of the machine.

Clean the plastic parts of the body with a damp sponge using water and detergent, taking care not to wet the engine, the electrical parts or the electronic card located under the dashboard.

Never use hose-nozzles or harsh detergents for cleaning the body and engine!

Do not let debris and dry remains of grass accumulate in upper part of the cutting deck in order to keep maximum machine efficiency and safety levels.

After each use, accurately clean the cutting deck to remove any grass remains or debris.

Wear eye protection and keep people or animals away

from the surrounding area when cleaning the cutting deck.

a) When washing the inside of the cutting deck and the collector channel, the machine must be on firm ground:

1. fit the grass-catcher;

2. connect a water hose to its pipe fitting (1), and run water through it;

3. sit at the operator’s position;

4. lower the cutting deck completely;

5. start the engine and stay in neutral;

6. engage the blade and leave it to turn for a few minutes.

b) To clean the upper part of the cutting deck:

– lower the cutting deck completely (position «1»);

– blow a jet of compressed air to remove any remains of grass.

5.4.9 Storage and inactivity for long periods

If the machine is likely to be unused for a long period (more than 1 month),，follow the instructions in the engine manual.

Empty the fuel tank by removing the screw situated at the bottom of the fuel filter (1), and collects the fuel in a suitable container.

Carefully remove any dry grass cuttings which may have collected around the engine or silencer to prevent their catching fire the next time the machine is used!

WARNIN                                                                    G!

Put the machine away in a dry, sheltered place and preferably covered with a cloth.

Disconnect the connectors (2 and 3) of the battery (1).

The battery must be kept in a cool and dry place. Before a long storage period (more than 1 month), always charge the battery, and then recharge before using again (☛ 6.2.3).

The next time the machine is used, check that there are no fuel leaks from the tubes or carburetor.

5.5 USING ON SLOPES

When mowing lawns on a slope, observe the maximum gradients already mentioned (max 10° - 17%) and move up and down but never across them. Take great care when changing direction that the highest wheels do not hit obstacles (such as stones, branches, roots, etc.) that may cause the machine to slide sideways, tip over or otherwise cause loss of control.

SLOW DOWN BEFORE CHANGING DIRECTION ON SLOPES. Never use reverse to reduce speed going downhill: you may lose control of the machine, particularly on slippery surfaces. Never ride the machine on slopes in neutral or with the clutch out! Always engage a low gear and the parking brake before leaving the machine at a stopped and unattended.

Take care when beginning forward movement on sloping ground to prevent the risk of tipping up. Reduce the forward speed before going on a slope, particularly downhill.

5.6 TRANSPORTING

If the machine is transported on a truck or trailer, use ramps with suitable resistance, width and length. Load the machine with the engine switched off, without a driver and pushed by an adequate number of people. During transport, close the fuel stopcock (if fitted), lower the cutting deck, engage the parking brake and fasten the machine securely with ropes or chains to the hauling device.

5.7 ADVICE ON HOW TO OBTAIN A GOOD CUT

1. To keep a lawn green and soft with a good appearance, it should be cut regularly without damaging the grass.

2. It is always better to cut the grass when dry.

3. The blade must be in good condition and well sharpened so that the grass is cut

straight without any ragged edge that leads to yellowing at the ends.

4. The engine must run at full speed, both to ensure a sharp cut of the grass and to get the

necessary thrust to push the cuttings through the collector channel.

5. The frequency of mowing should be in relation to the rate of growth of the grass, which should not be left to grow too much between one cut and the next.

6. During hot and dry periods, the grass should be cut a little higher to prevent the ground from drying out.

7. If the grass is very tall, it should be cut twice in a twenty four hour period. The first time at maximum cutting height, possibly reducing the cutting width and the second cut at the height desired.

8. The appearance of the lawn will improve if you alternate the cutting in both directions.

9. If the collector channel tends to get blocked with grass, you should reduce the forward speed since this may be too high for the condition of the lawn. If the problem persists, the probable causes are either the badly sharpened blade or deformed wings.

10. Be very careful when mowing near bushes or kerbs since these could distort the

horizontal position of the cutting deck, and damage its edge as well as the blade.

6.1 SAFETY RECOMMENDATIONS

Disconnect the spark plug cap, remove the key (in the electric start models) or shift the accelerator lever to «OFF» (in the manual start models) and read the relevant instructions before starting any cleaning, maintenance or repairs. Wear suitable clothing and strong gloves for dismantling and refitting the blade and in all other hazardous situations for the hands.

Never use the machine with worn or damaged parts. Faulty or worn-out parts must always be replaced and not repaired. Only use original spare parts: The use or non-original and/or incorrectly fitted parts will compromise the safety of the machine, may cause accidents or personal injuries for which the Manufacturer is under no circumstance liable or responsible.

Never get rid of used oil, fuel or other pollutants in unauthorized places!

Any adjustments or maintenance operations not described in this manual must be carried out by your Dealer or a specialized Service Centre. Both have the necessary knowledge and equipment to ensure

that the work is done correctly without affecting the safety of the machine.

You must go to a specialized Service Centre or contact your Dealer of the following are malfunctioning:

– the brake;

– the engagement and stop of the blade;

– the drive engagement in forward and in reverse gears.

6.2 ROUTINE MAINTENANCE

6.2.1 Engine

Follow all the instructions in the engine manual.

To drain the engine oil:

1. unscrew the topping up cap (1);

2. fit the pipe (2) onto the syringe (3) (on request)) and insert it

right into the hole;

3. using the syringe (3) (on request), suck up all the engine oil,

bearing in mind that you need to repeat this

operation a few times before all the oil is removed.

6.2.2 Transmission and gear unit

These are sealed single units which do not require maintenance. They are permanently lubricated and this lubricant does not need changing or topping up.

6.2.3 Battery

To ensure long life to the battery it is essential to keep it carefully maintained.

The machine battery must always be charged:

– before using the machine for the first time after purchase;

– before leaving the machine for a prolonged period of disuse;

– before starting up the machine after a prolonged period of disuse.

– to ensure long life to the battery it is essential to keep it carefully maintained. Failure in following the procedure or in charging the battery could permanently damage the battery elements.

– A flat battery must be recharged as soon as possible.

Recharging must be done using a battery charger at constant voltage. Other recharging systems can irreversibly damage the battery.

The machine comes with a connector (1) for recharging, near the battery, to be connected to the connector for the battery-charger supplied (if included) or available on request (☛9.2).

This connector must only be used for connecting to the battery charger. For its use:

6.3 INTERVENTIONS ON THE MACHINE

6.3.1 Cutting deck alignment

The cutting deck should be properly set to obtain a good cut.

If the cut is uneven, check the tire pressure.

If this is not sufficient to achieve an even cut,

please contact your Dealer for the adjustment

of the alignment of the cutting deck.

6.3.2 Replacing wheels                                                                                                                                 1. Place the machine on a flat surface and put blocks under a load-bearing part of the frame on the side of the wheel to be changed;

2. using a screwdriver, remove the snap ring (1);

3. pull out the wheel                                                                                                 Smear some waterproof grease on the axle and after refitting the wheel; carefully refit the washer (2) and the snap ring (1).

If you have to replace one or both rear wheels, make sure that any differences in their external diameter does not exceed 8-10 mm; on the contrary, to prevent an uneven cut it will be necessary to adjust the alignment of the cutting deck.

6.3.3 Replacing and repairing tires

All puncture repairs or replacements will have to be carried out by a tire repair expert in accordance with the methods for the kind of tire used.

6.3.4 Replacing a fuse

The electric system and the electronic card are protected by a fuse. When it blows the machine stops, so in this case:

1. remove the engine housing (1) using a hand;

2. replace the fuse (2) with another one with the same capacity;

3. remount the engine housing (1).

The fuse capacity is indicated on the fuse.

A blown fuse must always be replaced by one of the same type and ampere rating, and never with one of another rating.

If you cannot find out why the fuse has blown, consult a Licensed Service Centre.

The electric system and the card are not protected by any fuses. If the safety system fails to work properly or there are engine problems due to the electric system, contact a Licensed Service Centre.

6.3.5 Dismantling, replacing and remounting the blade

Always wear work gloves when handling the blade.

Damaged or bent blades must always be replaced; never try to repair them! ALWAYS USE MANUFACTURER'S GENUINE REPLACEMENT BLADES BEARING THE SYMBOL!

Environmental protection should be a priority of considerable importance when using the machine, for the benefit of both social coexistence and the environment in which we live.

– Try not to cause any disturbance to the surrounding area.

– Scrupulously comply with local regulations and provisions for the disposal of waste

– Scrupulously comply with local regulations and provisions for the disposal of oils, petrol, damaged parts or any elements which have a strong impact on the environment; this

waste must not be disposed of as normal waste, it must be separated and taken to specified waste disposal centers where the material will be recycled.

At the time of decommissioning, do not pollute the environment

PROBLEM LIKELY CAUSE SOLUTION 1.With the key on «START» Electronic card blocked due to: Turn the key to «STOP» and look for the cause the starter motor of the problem: does not run – flat battery – recharge battery (☛6.2.3) – fuse blown – replace fuse (10A) (☛6.3.4) – bad earthling to the engine or the frame – check connections of black earth leads – earth connections of the micro switches – check connections disconnected – badly earthed starter motor – check earth connections – you are not ready for starting (Safety Switches) – check that the conditions allowing the start are met (☛5.2.a)

2. With the key on «START» the –faulty fuel supply –check the level in the tank (☛5.3.3) Starter motor runs but the engine –check the wiring of the fuel open command does not start –check fuel filter –faulty ignition –check that spark plug caps are firmly fitted –check that the electrodes are clean and have the correct gap

3. The engine stops Electronic card blocked due to: Turn the key to pos. «OFF» and look for the cause of the problem: –earth connections of the micros witches –check connections disconnected –flat battery –recharge battery (☛6.2.3) –badly connected battery (poor contact) –check connections (☛3.5) –engine badly earthed –check engine earth connection

4. The engine does not start – earth connections of the micros witches –check connections disconnected – you are not ready for starting –check that the conditions allowing the start are met (☛5.2.a) 5. The engine stops –earth connections of the micro switches –check connections Disconnected

6. Starting is difficult or the –fault in carburetion –clean or replace the air filter engine runs erratically –flush out the float chamber –empty fuel tank and refill with fresh fuel –check and, if necessary, replace fuel filter

7. Weak engine performance –forward speed too high in relation to –reduce the forward speed and/or raise during cutting cutting height the cutting deck (☛5.4.5)

8. Engine stops when blade is engaged –you are not ready to engage the blade –check that the safety requirements are met(5.2.b) 9. Unusual vibrations while working –blade unbalanced –Contact your dealer –blade loose –Contact your dealer –fixing bolts loose –check and tighten all the fixing bolts of the engine and frame

10. Uncertain or ineffective braking –the brake is not adjusted correctly –Contact your Dealer

11. Uncertain or ineffective braking –the brake is not adjusted correctly –Contact your Dealer

Do not take on complicated repair work if you don't have the necessary equipment or the technical knowledge. The warranty is automatically voided and the manufacturer is not held responsible if repairs are done badly.

1. BATTERY-CHARGER

Battery charger charges the battery when the machine is in storage.

Note: The motor can be started manual (without battery) and the Battery will be charged automatically if the motor is working.

2. Change Blade

1.Make sure there is no machine oil and gasoline in the tank, side lay the machine as the picture above.

2. Loosen blade bolts and unscrew

3. Take the blade out and change the new one

4. Tighten bolt

5-6. Use the torque wrench to check if the torque is at least 40N.m.

Maximum noise and vibration levels

Operator ear noise pressure level

(according to regulation ISO 5395-1:2013, Annex F) ........................ 80.3dB(A)

– Measurement uncertainty (2000/14/EC) ...........................................2.5dB(A)

Measured acoustic output level

(according to directive ISO 5395-1:2013, Annex F) ….....................…97.02dB(A)

– Measurement uncertainty (2000/14/EC) ...........................................1.34 dB(A)

Guaranteed acoustic output level

(according to directive ISO 5395-1:2013, Annex F) ….........................98 dB(A)

Vibration level

Max. Whole-body vibration: .................................................................3.761m/s2.

Max. Hand-arm vibration (steering wheel): ..............................4.969m/s2,  K=1.5m/s2.

Engine type：

Electrical system.................................................................................. 12 V d.c.                                                          Battery...................................................................................................7 Ah

Max. Output power…............................................................................4.8kW

Speed....................................................................................................3000/min

Fuel tack capacity........................................................................1000ml

Front tires..............................................................................................10 x4.00

Rear tires .............................................................................................13 x 5.00                                                                                                    Front tire pressure.................................................................................1.8 bar

Rear tire pressure .................................................................................1.3 bar

Net weight.............................................................................................107kg

Cutter width……………………………......................…………………… 630mm (25")

Cutting width……………………………………......................……......... 610mm (24")

Cutting height....................................................................................... 30-70mm

Driving speed

in 1st .....................................................................................................1.5 km/h

in 2nd ....................................................................................................2.0 km/h

in 3rd .....................................................................................................3.0 km/h

in 4th ................................................................................................... 4.6 km/h

in Reverse ............................................................................................2.3 km/h

Packing dimension (cm)………………………………….........................148 x76 x83

Machine dimension (cm)………………………………........................…142 x 83 x106

- DECLARATION OF CONFORMITY

GB / DECLARATION OF CONFORMITY BUILDER SAS ZI, 32 rue Aristide Bergès – 31270 Cugnaux – France Tel : +33 (0)5.34.502.502 Fax : +33 (0)5.34.502.503 declares that the machines: RIDE-ON LAWN MOWER RAC6196PR-1 Serial No.: 20230111937-20230112008 the people name holding the technical file：Mr. Olivier Patriarca have been designed in compliance with the following standards: EN-ISO 5395-1:2013+A1: 2018, EN-ISO 5395-3:2013+A1:2017+A2:2018 EN-ISO 14982：2009 And in accordance with the following directives: Machine Directive 2006/42/EC EMC Directive 2014/30/EU EMISSION Directive (EU)2016/1628 Noise Directive 2000/14/EC Annex VI & 2005/88/EC Measured sound power level: 94.34dB(A) Guarantee sound power level :98dB(A) Notify body: Cugnaux, 01/01/2023 Philippe MARIE / PDG

# Text boxes

3

1

2

3

3

1

2

3

4

1

3

2

5

4

3

2

1

2

4.3

4.21

4.4

4.12

4.11

4.6

4.6.1

4.1

4.5

4.2

B

A

C

N

4

3

2

1

R

4.5

4.6

A

B

4.11

4.8

4.22

1

1

1

1

1

3

2

1

1

1

2

1

6

5

4

3

2

1