ORIGINAL INSTRUCTIONS

Electric Blower Vacuum Shredder 2600W

RAC2600EB-UK-A

INSTRUCTION MANUAL

WARNING: Read this manual carefully before use it.

BUILDER SAS

32, rue Aristide Bergès - ZI 31270 Cugnaux – France

MADE IN PRC 2019

1     APPLICATION .................................................................................. 8

2     DESCRIPTION (FIG. 1) .................................................................... 8

3     PACKAGE CONTENT LIST. ............................................................ 8

4     SYMBOLS  ...................................................................................... 9

5     GENERAL POWER TOOL SAFETY WARNINGS  ........................ 10

5.1     Working area .......................................................................................................10

5.2     Electrical safety...................................................................................................10

5.3     Personal safety ...................................................................................................10

5.4     Power tool use and care.....................................................................................11

5.5     Service.................................................................................................................11

6     SPECIFIC SAFETY INSTRUCTIONS  ........................................... 11

7     ASSEMBLY  ................................................................................... 12

7.1     Assembling the tubes (Fig. 2.1-2.4)....................................................................12

7.2     Assembling the collection bag support (Fig. 3) ...............................................12

7.3     Fitting the collection bag (Fig. 4.1 - 4.4) ............................................................12

7.4     Fitting the shoulder strap (Fig. 5.1&5.2).............................................................13

8     OPERATION ................................................................................. 13

8.1     Steps prior to operation......................................................................................13

8.2     Switching ON/OFF(Fig. 6.1 )...............................................................................13

8.3     Use/Operation .....................................................................................................13

8.4     Switching operating mode (Fig. 7.1 ).................................................................14

8.5     Collection bag .....................................................................................................14

9     RESIDUAL RISKS  ........................................................................ 15

10    CLEANING AND MAINTENANCE ................................................. 15

11    STORAGE ...................................................................................... 15

12    TROUBLE SHOOTING .................................................................. 15

13    TECHNICAL DETAILS ................................................................... 16

14    NOISE ............................................................................................. 16

15    WARRANTY ................................................................................... 16

16    RECYCLING ................................................................................... 16

FIG. 1

Fig. 2 : step 1 & 2

Fig. 2 : step 3 & 4

Fig. 2 : step 5 & 6

Fig. 3

Fig. 4

Fig 5

Fig. 6

Fi

ELECTRIC BLOWER VAC 3000W

1    APPLICATION

The blower/vacuum is designed to blow/vacuum leaves as well as lawn debris such as grass

clippings and small twigs. It is not to be used for any other purpose.  The device is only to be

used on dry surfaces.  The device is intended for non-commercial use in private home and

gardens.

This product is not designed for commercial, industrial or trade use.

WARNING! For  your  own safety,  read  this  manual  and  the general  safety instructions carefully  before  using the  appliance. Your  power tool  should only be given to other users together with these instructions.

2    DESCRIPTION (FIG. 1)

- Whell support

- Front blow/suction tube

- Rear blow/suction tube

- Additional adjustable handle

- Electric Blower Vac body

- Speed adjustment dial

- On/Off switch

- Collection bag support

- Collection bag

- Shoulder strap (Carrying belt)

- Power cable

3    PACKAGE CONTENT LIST.

▪    Remove all packaging materials.

▪    Remove remaining packaging and packing inserts (if included).

▪    Check that the package contents are complete.

▪    Check the appliance, the power cord, the power plug and all accessories for transportation

damage.

▪    Keep the packaging materials as far as possible until the end of the warranty period. Then

take it to your local waste disposal system.

WARNING  Packaging  materials are  not  toys!  Children  must  not play  with plastic bags! There is a danger of suffocation!

1 x Electric Blower Vac body

1 x Collection bag

1 x Collection bag support

1 x Front blow/suction tube

1 x Rear blow/suction tube

1 x Shoulder strap

1 x Screw 45mm

1 x Screw 75mm

1 x Wheel assembly

1 x Manual

1 x Warranty card

If any parts are missing or damaged, please contact SPARK.

4    SYMBOLS

The following symbols are used in this manual and/or on the machine:

5    GENERAL POWER TOOL SAFETY WARNINGS

Read all safety warnings and instructions. Failure to heed warnings and follow instructions

may result in electric shock, fire and/or serious injury. Keep safety warnings and instructions

for future reference. The term "power tool" in the safety warnings refers to your mains-

operated (corded) power tool or battery- operated (cordless) power tool.

5.1     Working area

▪Keep working area clean and well lit. Untidy and dark areas can lead to accidents.

▪Do not operate power tools in potentially explosive surroundings, for example, in the

presence of inflammable liquids, gases or dust. Power tools create sparks which may

ignite the dust or fumes.

▪Keep children and bystanders at a distance when operating a power tool. Distractions can

cause you to lose control of it.

5.2    Electrical safety

Always check that the power supply corresponds to the voltage on  the rating plate.

▪Power tool plugs must match the outlet. Never modify the plug in any way. Do not use

adapter plugs with earthed power tools. Unmodified plugs and matching outlets will  reduce the risk of an electric shock.

▪Avoid body contact with earthed surfaces such as pipes, radiators, kitchen ranges and

refrigerators. There is an increased risk of an electric shock if your body is earthed.

▪Do not expose power tools to rain or wet conditions. If water gets inside a power tool, it will

increase the risk of an electric shock.

▪Do not damage the cord. Never use the cord for carrying, pulling or unplugging the power

tool. Keep the cord away from heat, oil, sharp edges or moving parts. Damaged or entangled cords increase the risk of an electric shock. If a retractable cord is used, the

cord should be fully reeled out to avoid heating up.

▪If operating a power tool in a damp location is unavoidable, use a power supply protected

by a residual current device (RCD). Using an RCD reduces the risk of an electric shock.

5.3    Personal safety

▪Stay alert, watch what you are doing and use common sense when operating a power

tool. Do not use a power tool when you are tired or under the influence of drugs, alcohol or

medication. A moment of inattention when operating a power tool may result in serious

personal injury.

▪Use safety equipment. Always wear eye protection. Using safety equipment such as a

dust mask, non-skid safety shoes, a hard hat, or hearing protection whenever it is needed

will reduce the risk of personal injury.

▪Avoid accidental starts. Ensure the switch is in the off position before inserting the plug.

Carrying power tools with your finger on the switch or plugging in power tools when the

switch is in the on position makes accidents more likely.

▪Remove any adjusting keys or spanners before turning on the power tool. A spanner or key left attached to a rotating part of the power tool may result in personal injury

▪Do not reach out too far. Keep your feet firmly on the ground at all times. This will enable

you retain control over the power tool in unexpected situations.

▪Dress properly. Do not wear loose clothing or jewellery. Keep your hair, clothing and

gloves away from the power tool. Loose clothes, jewellery or long hair can become

entangled in the moving parts.

▪If there are devices for connecting dust extraction and collection facilities, please ensure

that they are attached and  used correctly. Using such devices can reduce dust-related

hazards.

5.4    Power tool use and care

▪Do not expect the power tool to do more than it can. Use the correct power tool for what

you want to do. A power tool will achieve better results and be safer if used in the context

for which it was designed.

▪Do not use the power tool if the switch cannot turn it on and off. A power tool with a broken

switch is dangerous and must be repaired.

▪Disconnect the plug from the power source before making adjustments, changing

accessories, or storing power tools. Such preventive safety measures reduce the risk of

starting the power tool accidentally.

▪Store power tools, when not in use, out of the reach of children and do not allow people

who are not familiar with the power tool or these instructions to operate it. Power tools are

potentially dangerous in the hands of untrained users.

▪Maintain power tools. Check for misalignment or jammed moving parts, breakages or any

other feature that might affect the operation of the power tool. If it is damaged, the power

tool must be repaired. Many accidents are caused by using poorly maintained power tools.

▪Use the power tool, accessories and cutting tools, etc., in accordance with these

instructions and in the manner intended for the particular type of power tool, taking into

account the working conditions and the work which needs to be done. Using a power tool

in ways for which it was not intended can lead to potentially hazardous situations.

5.5    Service

▪Your power tool should be serviced by a qualified specialist using only standard spare

parts. This will ensure that it meets the required safety standards.

6    SPECIFIC SAFETY INSTRUCTIONS

▪Make sure the power cord is kept behind and away from the device while you work.

▪Walk at a measured pace while operating the blower. DO NOT RUN.

▪Never direct the suction/blown air opening toward persons or animals.

▪The Blower Vacuum- must not be used or starting until it has been fully assembled.

▪If the power cord or extension cord are damaged while you work, unplug the blower

immediately.

▪Never use the power cord as a handle to lift or carry the device.

▪Use the blower in daylight or with adequate illumination.

▪Bear in mind that the force generated by an electrical device can make you lose your

balance. Therefore, make sure that your feet are firmly planted and that your body is well

balanced when you are operating the device.

▪Never operate the blower on damp or wet grass.

▪Using the blower on sloping areas: Do not work in areas with unduly steep slopes.

▪Use the blower as follows when working on slopes: Always position yourself horizontally to

the slope and make sure your feet are firmly planted.  Exercise particular caution

whenever you change directions while working on a slope.

▪Keep the air outlet unobstructed and clean at all times.

▪Advice on the use and type of extension cords to be used, (not lighter than the cord used

on appliance)

▪The operator or user is responsible for accidents or hazards occurring to other people or

their property.

▪Only use a weather proof extension cord fitted with a coupler according to I EC 60320-2-3.

▪Disconnect the appliance from the mains supply :

O    Whenever you leave the machine,

O    before clearing a blockage.

O    before checking, cleaning or working on the appliance,

O    if the appliance starts to vibrate abnormally.

▪Keep all cooling air inlets clear of debris.

▪Maintenance and storage :

O    Keep all nuts, bolts and screws tight to be sure the appliance is in safe working

condition.

O    Check the debris collector frequently for wear or deterioration.

O    Replace worn or damaged parts.

O    Use only genuine replacement parts and accessories.

O    Store the appliance only in a dry place.

▪While operating the appliance, always wear substantial footwear and long trousers.

▪Wear protective goggles while operating.

▪Wearing hearing protection during periods of extended operation is recommended

▪Never operate the appliance with defective guards or shields, or without safety devices, for

example debris collector in place.

7    ASSEMBLY

Your new electric blower vac requires very little assembly work before it is ready for use.

7.1    Assembling the tubes (Fig. 2.1- 2.6)

1. Slide the rear blow/suction tube(3) into the suction/blower housing and make sure it fits correctly and is fully inserted.

2. Secure it on both sides of the suction/blower housing with the one 75mm screws provided.

3. Insert the Whell support (1) into the front suction/blower tube(2) and make sure it fits correctly and is fully inserted.

4. Secure it with the Whell support screw provided

5. Insert the he front suction/blower tube(2) into the rear blow/suction tube(3). Make sure they

fit properly and are fully inserted.

- Secure both with the 45mm screws provided.

7.2    Assembling the collection bag support (Fig. 3)

Insert the collection bag support (8) into the fcollection bag (9) and make sure it fits correctly and is fully inserted.

Secure it with the string belt on collection bag has been tightened.

7.3    Fitting the collection bag (Fig. 4.1 - 4.4)

Before fitting the collection bag (9) ensure that the Vacuum/Blow selector lever of the additional adjustable handle(4) operates smoothly and that it is not obstructed by debris from previous use.

Locate the collection bag and fold back the opening with the adaptor connection inserted into

the holes on both sides of the discharge opening. Attach the front of the debris collection bag

to the underside of the suction-blower tube using the clip fitted to the collection bag.

7.4    Fitting the shoulder strap (Fig. 5.1&5.2)

The blower-vac is supplied with a shoulder strap (10).

The shoulder strap should be attached to the top of the main body of the blower-vac as

shown. The shoulder strap is provided to reduce fatigue and aid comfort when using the

blower-vac and can be worn in a position to suit the operator.

8    OPERATION

8.1    Steps prior to operation

Only operate the device after completely assembling it. Prior to each use, check the power

cord for signs of damage. Under no circumstances should the power cord be used if it shows

any signs of damage.

Ensure that the blower/vacuum is only connected to conventional sockets with a 240V

alternating current supply.

Never operate the Blower-vac without the debris collection bag fitted.

8.2    Switching ON/OFF  (Fig. 6.1 )

Press the On/Off switch (7) from OFF to ON position to start machine.

To stop the machine simply release the On / Off switch(7) to position OFF.

8.3    Use/Operation

▪The easiest way to use the blower/vac is to

place the shoulder strap in a comfortable

position over your shoulder and hold the

rear handle at hip height so that the

majority of the tool’s weight rests on the

rollers.

▪When using the blower/vac to pick up

leaves it is best to move the tool on its

rollers. This ensures that the blower/vac is

at the perfect height above the ground. The

blower/vac is designed only to pick up

leaves. To avoid any damage to the tool

that is not covered by the warranty, do not

use it to pick up branches, stones or other

hard materials.

▪When using the tool as a leaf blower

always work away from solid objects such

as walls, fences, etc. Whilst you work do

not place the blower/vac tube too close to

the leaves. The tool will be more effective if

you keep it at a certain distance away from

the leaves and blow the leaves forwards.

8.4    Switching operating mode (Fig. 7.1 )

To switch the tool from blower mode to vacuum mode, simply switch it off at the main switch

and move the function selector lever to the other position :

Lever to rear of machine (move lever upward) = vac. (suction)

Lever towards front of machine (move lever downward) = blow

As blower ：

Inspect the area to be worked before starting. Remove any objects that could be thrown,

jammed or become entangled in the blower-vac.

The blower-vac can be used to blow debris from patios, paths, driveways, lawns, bushes,

borders etc.

Work away from solid objects.

As Vac ：

Do not attempt to pick up wet debris, allow fallen leaves etc, to dry out first.

Your blower-vac will pick up leaves,  paper, small twigs and wood chippings. These are sucked

up the tube. Before being ejected into the collection bag, they pass through the suction fan and

are partially shredded. Shredded organic material is ideal to use as mulch around plants.

Warning! Any hard objects, such as stones, tin cans glass etc, will damage the

suction fan!

8.5    Collection bag

Note: Before you remove and empty the collection bag ensure that the tool has

been disconnected from the mains power supply.

To empty the collection bag simply open the zipper, empty the bag and then close the zipper

again.

When the collection bag is open you can also check the function of the blower vac’s slide

control. If there is a blockage in the tool, check this function and remove the blockage.

9    RESIDUAL RISKS

Even when the tool is used as prescribed it is not possible to eliminate all residual risk

factors.

The following hazards may arise in connection with the tool's construction and design:

▪Damage to lungs if an effective dust mask is not worn.

▪Damage to hearing if effective hearing protection is not worn.

▪Health defects resulting from vibration emission if the power tool is being used over longer

period of time or not adequately managed and properly maintained.

WARNING! This machine produces an electromagnetic field during operation.

This  field may  under  some  circumstances interfere  with  active or  passive medical implants. To reduce the risk of serious or fatal injury, we recommend persons  with medical  implants  to  consult their  physician  and  the medical implant manufacturer before operating this machine.

10    CLEANING AND MAINTENANCE

Attention! Before performing any work on the equipment, pull the power plug.

Keep the ventilation slots of the tool clean to prevent overheating of the engine.

Regularly clean the tool housing with a soft cloth, preferably after each use.

If the dirt does not come off use a soft cloth moistened with soapy water.

Never use solvents such as petrol, alcohol, ammonia water, etc. These solvents may

damage the plastic parts.

11    STORAGE

Never leave material in the blower-vac suction tube or collection bag.

12    TROUBLE SHOOTING

Please check below chart for the observed symptoms to solve problems with your machine

| Problem | Possible Cause | Action |
| --- | --- | --- |
| The engine does not start | The machine is not connected to the mains | Plug the machines to the mains. |
|  | Damaged cable | Take the machine to the after sales agent. Never repair the cable with tape. |
|  | The machine is not completely mounted | Mount the tubes and the catcher. |
|  | Damaged switch | Take the machine to the after sales service |
| The machine does not blow | The lever of the machine is on vacuum mode. | Put the lever on the blowing position. |
|  | Ventilator obstructed. | Remove the tube and clean the ventilator. |
|  | Tubes obstructed | Clean the tubes |
| The machine does not vacuum | The lever is on blowing mode. | Put the lever on the vacuum position. |
|  | Ventilator obstructed. | Remove the tube and clean the ventilator. |
|  | Tubes obstructed. | Clean the tubes |

If the problem cannot be solved using above chart than please contact your after sales agent.

13    TECHNICAL DETAILS

| Model nr. | RAC2600EB-UK-A |
| --- | --- |
| Voltage / frequency : | 230-240V~ 50Hz |
| Power | 2600W |
| No load speed : | 8000-14000 RPM |
| Air speed | 120-240 km/h |
| Max air volume | 13 m³/min |
| collection bag | 35 L |
| Shredding ratio : | 10:1 |

14    NOISE

Noise values measured according to relevant standard. (K=3)

| Acoustic pressure level LpA | 97.2 dB(A) |
| --- | --- |
| Acoustic power level LwA | 104 dB(A) |

ATTENTION!  The  sound  power  level  may  exceed   85  dB(A),  in  this  case individual hearing protection shall be worn.

| aw (Vibration) | 3.7 m/s² | K = 1,5 m/s² |
| --- | --- | --- |

15    WARRANTY

Refer to enclosed warranty conditions for terms and conditions.

16    RECYCLING

Should your appliance need  replacement after extended use, do  not dispose of it

with the household refuse, but in an environmentally safe way.

Waste electrical products should not be disposed of with household waste. Please

recycle where facilities exist. Check with your Local Authority or retailer for recycling advice.

GB / DECLARATION OF CONFORMITY

BUILDER

ZI, 32 rue aristide Bergès – 31270 Cugnaux - France

Tel  : +33 (0)5.34.502.502   Fax : +33 (0)5.34.502.503

declares that the machines:

Electric Blower Vacuum Shredder 2600W

Model: RAC2600EB-UK-A

Serial No.: from XXXXXX to XXXXXX

the people name holding the technical file：Mr.Olivier Patriarca

have been designed in compliance with the following standards:

EN 60335-1:2012 + A11:2014 + A13:2017

EN 50636-2-100:2014; EN 62233:2008

EN 55014-1:2017; EN 61000-3-2:2014

EN 61000-3-3:2013; EN 55014-2:2015

EN ISO 3744:2010 & ISO 10884:1995

And in accordance with the following directives:

Directive Machine 2006/42/EC

Directive EMC 2014/30/EU

noise Directive 2000/14/EC Annex V & Directive 2005/88/EC

Measured sound power level LwA dB(A)         Brush cutter: 101 dB (A)

(According to ISO 22868)                      K=3 dB (A)

Guaranteed sound power level                  104 dB (A)

(According to ISO 2000/14/EC)

Philippe MARIE / PDG

Cugnaux, 27-09-2019

# Text boxes

Denotes risk of personal injury or

damage to the tool.

Wear eye protection

RCM- logo means this item applied for RCM. (Regulatory Compliance Mark ).  The item is compliant to any ACMA regulatory arrangement. (ACMA : Australian Communications and media Authorities)

WARNING!

A special warning on long hair : Severe injury can occur!

▪If  your hair is longer than shoulder-length, you must make sure it

is securely tied up prior to you using the power tool!

▪Keep  your hair away from the power tool.

▪Long  hair can become entangled in the moving parts.

Keep bystanders away.

There is a risk that stones or other objects will be thrown out of the

device. Keep a safe distance from other people or pets.

Sound power level

Double insulated

Do not operate in rain

Switch off and unplug

the device before

cleaning or performing

maintenance on it.

Wear hearing

protection

Read manual before use

Disconnect from the mains supply if a cable is damaged or entangled

Wear  respiratory

protection

Rotating fan blades. Can cause serious injury or cut.  Keep hands clear. Switch off and unplug the device before

servicing.